## Slide 1: Digital Image Processing
Lecture 5
DCT & Wavelets
Tammy Riklin Raviv
Electrical and Computer Engineering
Ben-Gurion University of the Negev

## Slide 2: Spatial Frequency Analysis
images of naturally occurring scenes or objects (trees, rocks,
bushes, etc.) tend to contain information at many different spatial
scales, from very fine to very coarse.
see the forest for the trees
Can’t

## Slide 3: Spatial Frequency Analysis
Campbell-Robson contrast sensitivity curve
http://www.psy.vanderbilt.edu/courses/hon185/SpatialFrequency/SpatialFrequency.html

## Slide 4: This class
Why transform?
Discrete Cosine Transform
Jpeg Compression
Wavelets

## Slide 5: why transform?
Better image processing
  Take into account long-range correlations in space
  Conceptual insights in spatial-frequency information. what it means to be “smooth, moderate change, fast change, …”
  Denoising

## Slide 6: why transform?
Better image processing
  Take into account long-range correlations in space
  Conceptual insights in spatial-frequency information. what it means to be “smooth, moderate change, fast change, …”
  Denoising
Fast computation: convolution vs. multiplication

## Slide 7: why transform?
Better image processing
  Take into account long-range correlations in space
  Conceptual insights in spatial-frequency information. what it means to be “smooth, moderate change, fast change, …”
  Denoising
  Fast computation: convolution vs. multiplication
Alternative representation and sensing
  Obtain transformed data as measurement in radiology images (medical and astrophysics), inverse transform to recover image

## Slide 8: why transform?
Better image processing
  Take into account long-range correlations in space
  Conceptual insights in spatial-frequency information. what it means to be “smooth, moderate change, fast change, …”
  Denoising
Fast computation: convolution vs. multiplication
Alternative representation and sensing
  Obtain transformed data as measurement in radiology images (medical and astrophysics), inverse transform to recover image
Efficient storage and transmission
  Energy compaction
  Pick a few “representatives” (basis)
  Just store/send the “contribution” from each basis
?

## Slide 9: Is DFT a Good (enough) Transform?
Theory
Implementation
Application

## Slide 10: The Desirables for Image Transforms
Theory
  Inverse transform available
  Energy conservation (Parsevell)
  Good for compacting energy
  Orthonormal, complete basis
  (sort of) shift- and rotation invariant
Implementation
  Real-valued
  Separable
  Fast to compute w. butterfly-like structure
  Same implementation for forward and inverse transform
Application
  Useful for image enhancement
  Capture perceptually meaningful structures in images
DFT
???
X X ? X X
x X X X
X X

## Slide 11: Discrete Cosine Transform - overview
One-dimensional DCT
Orthogonality
Two-dimensional DCT
Image Compression (grayscale, color)

## Slide 12: Discrete Cosine Transform (DCT)
A variant of the Discrete Fourier Transform – using only real numbers
Periodic and symmetric
The energy of a DCT transformed data (if the original data is correlated) is concentrated in a few coefficients – well suited for compression.
A good approximation to the optimal Karhunen-Loeve (KL) decomposition of natural image statistics over a small patches

## Slide 13: 1-D DCT

## Slide 14: 1-D DCT with Matlab

## Slide 15: 1-D DCT with Matlab

## Slide 16: 1-D Inverse DCT in Matlab

## Slide 17: 1-D Inverse DCT in Matlab

## Slide 18: 1-D Inverse DCT in Matlab

## Slide 19: 1-D Inverse DCT in Matlab

## Slide 20: 1-D Inverse DCT in Matlab

## Slide 21: 1-D Inverse DCT in Matlab

## Slide 22: 1-D Inverse DCT in Matlab

## Slide 23: 1-D Inverse DCT in Matlab

## Slide 24: Orthogonality and Orthonormality
Two vectors, and , with respective lengths
are orthogonal if and only if their dot product
is zero.
In addition, two vectors in an inner product space are
orthonormal if they are orthogonal and both of unit length.

## Slide 25: Orthogonality of the DCT

## Slide 26: DFT vs. DCT
1D-DFT
real(a)
imag(a)
1D-DCT

## Slide 27: DFT vs. DCT – Matrix notation
1D-DFT
1D-DCT
real(C)
imag(C)
N=32

## Slide 28: DCT Properties
is real and orthogonal:
The rows of form an orthogonal basis.
is not symmetric!
DCT is not the real part of unitary DFT!

## Slide 29: The Advantage of Orthogonality
is orthogonal.
Makes matrix equation solving easy:

## Slide 30: The Advantage of Orthogonality
The discrete cosine transform, C, has one basic characteristic: it is a real orthogonal matrix.

## Slide 31: From 1D-DCT to 2D-DCT

## Slide 32: 2D DCT
Like the 2D Fast Fourier Transform, the 2D DCT can be implemented in two stages, i.e., first
computing the DCT of each line in the block and then computing the DCT of each resulting column.
Like the FFT, each of the DCTs can also be computed in O(N logN) time.

## Slide 33: DCT in Matlab

## Slide 34: DCT in Matlab

## Slide 35: DCT in Matlab

## Slide 36: 2D - DCT
Idea 2D-DCT: Interpolate the data with a set of basis functions
Organize information by order of importance to the human visual system
Used to compress small blocks of an image
(8 x 8 pixels in our case)

## Slide 37: 2D DCT
Use One-Dimensional DCT in both horizontal and vertical directions.
First direction F = C*XT
Second direction G = C*FT
We can say 2D-DCT is the matrix:
Y = C(CXT)T

## Slide 38: 2D DCT

## Slide 39: basis images: DFT (real) vs DCT
DFT
DCT

## Slide 40: Periodicity Implied by DFT and DCT

## Slide 41: DFT and DCT
DFT2
DCT2
Shift low-freq to the center
Assume periodic and zero-padded …
Assume reflection …

## Slide 42: Image Compression
Image compression is a method that reduces the amount of memory it takes to store in image.
We will exploit the fact that the DCT matrix is based on our visual system for the purpose of image compression.
This means we can delete the least significant values without our eyes noticing the difference.

## Slide 43: Image Compression
Now we have found the matrix Y = C(CXT)T
Using the DCT, the entries in Y will be organized based on the human visual system.
The most important values to
our eyes will be placed in the
upper left corner of the matrix.
The least important values
will be mostly in the lower
right corner of the matrix.

## Slide 44: Common Applications
JPEG Format
MPEG-1 and MPEG-2
MP3, Advanced Audio Coding, WMA
What’s in common?
  All share, in some form or another, a DCT method for compression.
Joint Photographic Experts Group

## Slide 45: Lossy Image Compression (JPEG)
Block-based Discrete Cosine Transform (DCT)

## Slide 46: Using DCT in JPEG
The first coefficient B(0,0) is the DC component, the average intensity
The top-left coeffs represent low frequencies, the bottom right – high frequencies

## Slide 47: Image compression using DCT
DCT enables image compression by concentrating most image information in the low frequencies
Loose unimportant image info (high frequencies)
The decoder computes the inverse DCT – IDCT

## Slide 48: Block size in JPEG
Block size
  small block
    faster
    correlation exists between neighboring pixels
  large block
    better compression in smooth regions
  It’s 8x8 in standard JPEG

## Slide 49: Image Compression
8 x 8 Pixels Image

## Slide 50: Image Compression
Gray-Scale Example:
Value Range 0 (black) --- 255 (white)
63 33 36 28 63 81 86 98
27 18 17 11 22 48 104 108
72 52 28 15 17 16 47 77
132 100 56 19 10 9 21 55
187 186 166 88 13 34 43 51
184 203 199 177 82 44 97 73
211 214 208 198 134 52 78 83
211 210 203 191 133 79 74 86
X

## Slide 51: Image Compression
2D-DCT of matrix
-304 210 104 -69 10 20 -12 7
-327 -260 67 70 -10 -15 21 8
93 -84 -66 16 24 -2 -5 9
89 33 -19 -20 -26 21 -3 0
-9 42 18 27 -7 -17 29 -7
-5 15 -10 17 32 -15 -4 7
10 3 -12 -1 2 3 -2 -3
12 30 0 -3 -3 -6 12 -1
Numbers are coefficients of polynomial
Y

## Slide 52: Image Compression
Cut the least significant components
-304 210 104 -69 10 20 -12 0
-327 -260 67 70 -10 -15 0 0
93 -84 -66 16 24 0 0 0
89 33 -19 -20 0 0 0 0
-9 42 18 0 0 0 0 0
-5 15 0 0 0 0 0 0
10 0 0 0 0 0 0 0
0 0 0 0 0 0 0 0
As you can see, we save a little over half the original memory.

## Slide 53: Reconstructing the Image
New Matrix and Compressed Image
55 41 27 39 56 69 92 106
35 22 7 16 35 59 88 101
65 49 21 5 6 28 62 73
130 114 75 28 -7 -1 33 46
180 175 148 95 33 16 45 59
200 206 203 165 92 55 71 82
205 207 214 193 121 70 75 83
214 205 209 196 129 75 78 85

## Slide 54: Can You Tell the Difference?
Original Compressed

## Slide 55: Image Compression
Original Compressed

## Slide 56: Linear Quantization
We will not zero the bottom half of the matrix.
The idea is to assign fewer bits of memory to store information in the lower right corner of the DCT matrix.

## Slide 57: Linear Quantization
Use Quantization Matrix (Q)
qkl = 8p(k + l + 1) for 0 < k, l < 7
Q = p * 8 16 24 32 40 48 56 64
16 24 32 40 48 56 64 72
24 32 40 48 56 64 72 80
32 40 48 56 64 72 80 88
40 48 56 64 72 80 88 96
48 56 64 72 80 88 96 104
56 64 72 80 88 95 104 112
64 72 80 88 96 104 112 120

## Slide 58: Linear Quantization
p is called the loss parameter
It acts like a “knob” to control compression
The greater p is the more you compress the image

## Slide 59: Linear Quantization
We divide the each entry in the DCT matrix by the Quantization Matrix
-304 210 104 -69 10 20 -12 7
-327 -260 67 70 -10 -15 21 8
93 -84 -66 16 24 -2 -5 9
89 33 -19 -20 -26 21 -3 0
-9 42 18 27 -7 -17 29 -7
-5 15 -10 17 32 -15 -4 7
10 3 -12 -1 2 3 -2 -3
12 30 0 -3 -3 -6 12 -1
8 16 24 32 40 48 56 64
16 24 32 40 48 56 64 72
24 32 40 48 56 64 72 80
32 40 48 56 64 72 80 88
40 48 56 64 72 80 88 96
48 56 64 72 80 88 96 104
56 64 72 80 88 95 104 112
64 72 80 88 96 104 112 120

## Slide 60: Linear Quantization
p = 1 p = 4
-38 13 4 -2 0 0 0 0
-20 -11 2 2 0 0 0 0
4 -3 -2 0 0 0 0 0
3 1 0 0 0 0 0 0
0 1 0 0 0 0 0 0
0 0 0 0 0 0 0 0
0 0 0 0 0 0 0 0
0 0 0 0 0 0 0 0
-9 3 1 -1 0 0 0 0
-5 -3 1 0 0 0 0 0
1 -1 0 0 0 0 0 0
1 0 0 0 0 0 0 0
0 0 0 0 0 0 0 0
0 0 0 0 0 0 0 0
0 0 0 0 0 0 0 0
0 0 0 0 0 0 0 0
0 0 0 0 0 0 0 0
New Y: 14 terms New Y: 10 terms

## Slide 61: Linear Quantization
p = 1 p = 4

## Slide 62: Linear Quantization
Compressed with P=1
Compressed with P=4

## Slide 63: Linear Quantization
p = 1

## Slide 64: Linear Quantization
P= 4

## Slide 65: Quantization Example

## Slide 66: Further Compression
Run-Length Encoding (RLE)
Huffman Coding

## Slide 67: Memory Storage
The original image uses one byte (8 bits) for each pixel. Therefore, the amount of memory needed for each 8 x 8 block is:
  8 x (82) = 512 bits

## Slide 68: Is This Worth the Work?
The question that arises is “How much memory does this save?”
p | Total bits | Bits/pixel
X | 512 | 8
1 | 249 | 3.89
2 | 191 | 2.98
3 | 147 | 2.30
Linear Quantization

## Slide 69: JPEG Imaging
It is fairly easy to extend this application to color images.
  These are expressed in the RGB color system.
  Each pixel is assigned three integers for each color intensity.

## Slide 70: RGB Coordinates

## Slide 71: The Approach
There are a few ways to approach the image compression.
  Repeat the discussed process independently for each of the three colors and then reconstruct the image.
  Baseline JPEG uses a more delicate approach.
    Define the luminance coordinate to be:
      Y = 0.299R + 0.587G + 0.114B
    Define the color differences coordinates to be:
      U = B – Y
      V = R – Y

## Slide 72: More on Baseline
This transforms the RGB color data to the YUV system which is easily reversible.
It applies the DCT filtering independently to Y, U, and V using the quantization matrix QY.
B
G
R
V
U
Y

## Slide 73: JPEG Quantization
QY =
p { 16 11 10 16 24 40 51 61
12 12 14 19 26 58 60 55
14 13 16 24 40 57 69 56
14 17 22 29 51 87 80 62
18 22 37 56 68 109 103 77
24 35 55 64 81 104 113 92
49 64 78 87 103 121 120 101
72 92 95 98 112 100 103 99}
Luminance:

## Slide 74: JPEG Quantization
QC =
{ 17 18 24 47 99 99 99 99
18 21 26 66 99 99 99 99
24 26 56 99 99 99 99 99
47 66 99 99 99 99 99 99
99 99 99 99 99 99 99 99
99 99 99 99 99 99 99 99
99 99 99 99 99 99 99 99
99 99 99 99 99 99 99 99}
Chrominance:

## Slide 75: Luminance and Chrominance
Human eye is more sensible to luminance
(Y coordinate).
It is less sensible to color changes
(UV coordinates).
Then: compress more on UV !
Consequence: color images are more compressible than grayscale ones

## Slide 76: Reconstitution
After compression, Y, U, and V, are recombined and converted back to RGB to form the compressed color image:
B= U+Y
R= V+Y
G= (Y- 0.299R - 0.114B) / 0.587

## Slide 77: Comparing Compression
Original
p = 1
p = 4
p = 8

## Slide 78: Up Close

## Slide 79: JPEG compression comparison
89k
12k
See also
https://en.wikipedia.org/wiki/JPEG

## Slide 80: Wavelets - overview
Why wavelets?
Wavelets like basis components.
Wavelets examples.
Fast wavelet transform .
Wavelets like filter.
Wavelets advantages.

## Slide 81
Fourier Analysis
Breaks down a signal into constituent sinusoids of different frequencies
In other words: Transform the view of the signal from time-base to frequency-base.

## Slide 82
What’s wrong with Fourier?
By using Fourier Transform , we loose the time information : WHEN did a particular event take place ?
FT can not locate drift, trends, abrupt changes, beginning and ends of events, etc.
Calculating use complex numbers.

## Slide 83: Time and Space definition
Time – for one dimension waves we start point shifting from source to end in time scale .
Space – for image point shifting is two dimensional .
Here they are synonyms .

## Slide 84: Kronneker function
Can exactly show the time of appearance but have not information about frequency and shape of signal.

## Slide 85
Short Time Fourier Analysis
In order to analyze small section of a signal, Denis Gabor (1946), developed a technique, based on the FT and using windowing : STFT

## Slide 86
STFT (or: Gabor Transform)
A compromise between time-based and frequency-based views of a signal.
both time and frequency are represented in limited precision.
The precision is determined by the size of the window.
Once you choose a particular size for the time window - it will be the same for all frequencies.

## Slide 87
What’s wrong with Gabor?
Many signals require a more flexible approach - so we can vary the window size to determine more accurately either time or frequency.

## Slide 88
What is Wavelet Analysis ?
And…what is a wavelet…?
A wavelet is a waveform of effectively limited duration that has an average value of zero.

## Slide 89: Wavelet's properties
Short time localized waves with zero integral value.
Possibility of time shifting.
Flexibility.

## Slide 90
The Continuous Wavelet Transform (CWT)
A mathematical representation of the Fourier transform:
Meaning: the sum over all time of the signal f(t) multiplied by a complex exponential, and the result is the Fourier coefficients F() .

## Slide 91
Wavelet Transform (Cont’d)
Those coefficients, when multiplied by a sinusoid of appropriate frequency , yield the constituent sinusoidal component of the original signal:

## Slide 92
Wavelet Transform
And the result of the CWT are Wavelet coefficients .
Multiplying each coefficient by the appropriately scaled and shifted wavelet yields the constituent wavelet of the original signal:

## Slide 93
Scaling
Wavelet analysis produces a time-scale view of the signal.
Scaling means stretching or compressing of the signal.
scale factor (a) for sine waves:

## Slide 94
Scaling (Cont’d)
Scale factor works exactly the same with wavelets:

## Slide 95: CWT

## Slide 96: Wavelet function 1D -> 2D
b – shift coefficient
a – scale coefficient
2D function
(
)
(
)
a
b
x
x
b
a
-
Y
=
Y
a
1
,

## Slide 97
CWT
Reminder: The CWT Is the sum over all time of the signal, multiplied by scaled and shifted versions of the wavelet function
Step 1:
Take a Wavelet and compare
it to a section at the start
of the original signal

## Slide 98
CWT
Step 2:
Calculate a number, C, that represents how closely correlated the wavelet is
with this section of the signal. The
higher C indicates higher similarity.

## Slide 99
CWT
Step 3: Shift the wavelet to the right and repeat steps 1-2 until you’ve covered the whole signal

## Slide 100
CWT
Step 4: Scale (stretch) the wavelet and repeat steps 1-3

## Slide 101: Wavelets examples Dyadic transform
For easier calculation we can discretize a continuous signal.
We have a grid of discrete values that called dyadic grid .
Important: wavelet functions are compact (e.g. no overcalculatings) .

## Slide 102: Haar Wavelets

## Slide 103: Haar Wavelets Properties I
Any continuous real function with compact support can be approximated uniformly by linear combination of:
and their shifted functions

## Slide 104: Haar Wavelets Properties II
Any continuous real function on [0, 1] can be approximated uniformly on [0, 1] by linear combinations of the constant function
and their shifted functions

## Slide 105: Haar transform

## Slide 106: Haar Wavelets Properties III
Orthogonality

## Slide 107: Haar Wavelets Properties
Functional relationship:
It follows that coefficients of scale n can be calculated by
coefficients of scale n+1:

## Slide 108: Haar Matrix

## Slide 109: Wavelet functions examples
Haar function
Daubechies function

## Slide 110
Properties of Daubechies wavelets I. Daubechies, Comm. Pure Appl. Math. 41 (1988) 909.
Compact support
  finite number of filter parameters / fast implementations
  high compressibility
  fine scale amplitudes are very small in regions where the function is smooth / sensitive recognition of structures
Identical forward / backward filter parameters
  fast, exact reconstruction
  very asymmetric

## Slide 111
Mallat* Filter Scheme
Mallat was the first to implement this scheme, using a well known filter design called “two channel sub band coder”, yielding a ‘Fast Wavelet Transform’

## Slide 112
Approximations and Details:
Approximations: High-scale, low-frequency components of the signal
Details: low-scale, high-frequency components
Input Signal
LPF
HPF

## Slide 113
Decimation
The former process produces twice the data it began with: N input samples produce N approximations coefficients and N detail coefficients.
To correct this, we Down sample (or: Decimate) the filter output by two, by simply throwing away every second coefficient.

## Slide 114
Decimation (cont’d)
Input Signal
LPF
HPF
A*
D*
So, a complete one stage block looks like:

## Slide 115
Multi-level Decomposition
Iterating the decomposition process, breaks the input signal into many lower-resolution components: Wavelet decomposition tree:

## Slide 116
Wavelets and Pyramid
pyramid—each wavelet level stores 3/4
of the original pixels (usually the horizontal, vertical, and mixed gradients), so that the total
number of wavelet coefficients and original pixels is the same.

## Slide 117
2D Wavelet Decomposition

## Slide 118
2D Wavelet Decomposition

## Slide 119
2D Wavelet transform

## Slide 120
2D Wavelet transform

## Slide 121
2D Wavelet transform – Jpeg2000

## Slide 122: Orthogonality
For 2 vectors
For 2 functions

## Slide 123: Why wavelets have orthogonal base ?
It easier calculation.
When we decompose some image and calculating zero level decomposition we have accurate values .
Scalar multiplication with other base function equals zero.

## Slide 124
Wavelet reconstruction
Reconstruction (or synthesis) is the process in which we assemble all components back
Up sampling
(or interpolation) is done by zero inserting between every two coefficients

## Slide 125: Wavelets like filters
Relationship of Filters to Wavelet Shape
Choosing the correct filter is most important.
The choice of the filter determines the shape of the wavelet we use to perform the analysis.

## Slide 126
Example
A low-pass reconstruction filter (L’) for the db2 wavelet:
The filter coefficients (obtained by Matlab dbaux command:
0.3415 0.5915 0.1585 -0.0915
reversing the order of this vector and multiply every second coefficient by -1 we get the high-pass filter H’:
-0.0915 -0.1585 0.5915 -0.3415

## Slide 127
Example (Cont’d)
Now we up-sample the H’ coefficient vector:
-0.0915 0 -0.1585 0 0.5915 0 -0.3415 0
and Convolving the up-sampled vector with the original low-pass filter we get:

## Slide 128
Example (Cont’d)
Now iterate this process several more times, repeatedly up-sampling and convolving the resultant vector
with the original
low-pass filter,
a pattern
begins to
emerge:

## Slide 129
Example: Conclusion
The curve begins to look more like the db2 wavelet: the wavelet shape is determined entirely by the coefficient Of the reconstruction filter
You can’t choose an arbitrary wavelet waveform if you want to be able to reconstruct the original signal accurately!
https://www.mathworks.com/examples/wavelet

## Slide 130
https://www.mathworks.com/examples/wavelet
Wavelets in Matlab

## Slide 131
Compression Example
A two dimensional (image) compression, using 2D wavelets analysis.
The image is a Fingerprint.
FBI uses a wavelet technique to compress its fingerprints database.

## Slide 132
Fingerprint compression
Wavelet: Haar
Level:3

## Slide 133
Results
Original Image Compressed Image
Threshold: 3.5
Zeros: 42%
Retained energy:
99.95%

## Slide 134
Next Class
Principal Component Analysis
Geometric Transformations